## Slide 1: Ship motion prediction with IMU-data and images
Lance De Waele

## Slide 2: Contents
Introduction
Goal & Incentive
Data
Deep learning
Proposed Models
Performance & Results
Conclusion

## Slide 3: Introduction
Royal Military Academy
Robotics & Autonomous Systems lab
Marsur
  Developing an autonomous surface vessel (ASV)
Marland
  Developing an autonomous drone (UAV)
  Take-off and landing on moving vessels

## Slide 4: Goal & Incentive
Predict the motion of the ASV
Define optimal moment to land drone
  Landing deck stabile and level
  Minimal impact
Deep learning approach
Prediction:
  Sequence of Pitch, Roll and Heave
  Minimum 30 seconds

## Slide 5: Data
Ship motion in 6 degrees of freedom
  Translational
    Sway
    Surge
    Heave
  Rotational
    Yaw
    Pitch
    Roll

## Slide 6: Simulated data
540 episodes of 400 images
Rendered at 2 frames/second
  Avoid duplicate data at higher fps
  30 hours of simulation
Resolution 96x54
Pitch & roll per image
₁Source: https://github.com/Nazotron1923/ship-ocean_simulation_BLENDER

## Slide 7: Real data
Live video
Live IMU data
Additionally
  Wind sensor data
  Thrust (ASV)
Challenges
  Find optimal fps
  Objects in images
  Stabilization
  Noise
  …

## Slide 8: Deep learning

## Slide 9: Deep learning
Neural networks
Layers of neurons
Neurons learn
  Weight (w)
  Bias (b)
  Y = w*x + b
x
Y
w
b

## Slide 10: Deep learning
IMU data
Predicted sequence
Input
Hidden
Output

## Slide 11: Deep learning

## Slide 12: Deep learning models
Continuous data -> linear regression
  <-> logistic regression
Sequences -> LSTM
  Feedback connections
Images -> CNN
  Moving image kernels
  https://setosa.io/ev/image-kernels/
=> Together strong

## Slide 14: Some results

## Slide 15: Some results

## Slide 16: Some results

## Slide 17: Some results

## Slide 18: Some results
MODEL (input/output) | Avg. PITCH error (°) | Avg. ROLL error (°)
60/60 LSTM | 2.23° | 1.96°
10/60 LSTM | 5.18° | 4.66°
10/60 CNN-LSTM | 1.51° | 1.46°
10/60 Zero | 6.33° | 7.43°

## Slide 19: Questions