## Slide 1: Ship motion prediction with IMU-data and images
Lance De Waele
Supervisors:
Prof. dr. ir. Hiep Luong
Prof. dr. ir. Jan Aelterman
Counselors:
Charles Hamesse
Ir. Tien-Thanh Nguyen (Royal Military Academy)
Dr. ir. Benoit Pairet (Royal Military Academy)

## Slide 2: Contents
Introduction
Goal & Incentive
Data
Deep learning
Proposed models
Results
Conclusion

## Slide 3: Introduction
Royal Military Academy
Robotics & Autonomous Systems lab
MarLand
  Developing an autonomous drone
  Vertical Take-off and Landing (VTOL) on Belgian navy vessels
Notes: The Robotics & Autonomous Systems lab is a research unit of the department of Mechanics of the Belgian Royal Military Academy.

## Slide 4: Goal & Method
Safe VTOL procedures:
  Drone and surroundings
  Landing deck stabile and level
  Minimize impact
Predict motion of the vessel
  Anticipate movements
Requirements:
  Optimized for application
  Minimum 30 seconds
  Low latency & HW requirements

## Slide 5: Ship Motion
Six degrees of freedom (DoF)
  Translational
    Sway
    Surge
    Heave

## Slide 6: Ship Motion
Six degrees of freedom (DoF)
  Translational
    Sway
    Surge
    Heave
  Rotational
    Yaw
    Pitch
    Roll

## Slide 7: Conditions
Inertial Measurement Unit (IMU)
  Translational
  Rotational
Stereo Camera
  Incoming waves

## Slide 8: Simulated data
540 episodes of 400 images
Rendered at 2 frames/second (2Hz)
  Overlap, processing demand
  Aliasing <-> Accuracy
  30 hours of simulation
Resolution 96x54
Pitch & Roll (PR) per image
No heave?
₁Source: https://github.com/Nazotron1923/ship-ocean_simulation_BLENDER
Notes: Why only pitch and roll is enough:
Drone has large range of motion in heave but very small window in vertical hover pitch and roll
Lightweight drone with low inertia/high thrust can heave up/down based on measurements in real time

## Slide 9: Properties
Property | Pitch | Roll
Count | 216.000 | 216.000
Mean | 0,07° | 0,30°
Median | 0,03° | 0,23°
st. dev. | 6,6° | 7,1°
Min | -53,7° | -58,8°
Max | 61,3° | 62,2°
Notes: First, count: 540 episodes, each with 400 frames equals to 216k total images
Second, mean and median are equal, near zero
Third, stdev from roll is slightly higher than pitch => more spread-out values
Minimum and maximum similar and

## Slide 10: Properties
99.7% : µ ± 3σ ≈ [-20°, 20°]
216.000
Notes: Both pitch and roll are normally distributed, 99.7% in interval [-20°, 20°]

## Slide 11: Pre-processing

## Slide 12: Deep learning

## Slide 13: Deep learning
Neural networks
Layers of neurons
Neurons learn
  Weight (w)
  Bias (b)
  Y = wx + b
x
Y

## Slide 14: Deep learning
IMU data
Predicted sequence
Input
Hidden
Output

## Slide 15: Neural network architectures
Continuous data -> linear regression
  <-> logistic regression
Time series data -> LSTM
  Feedback connections
Images -> CNN
  Moving image kernels

## Slide 16: Optimal architecture?
Inputs ?
Hidden layers ?
Hyperparameters ?
Input
Hidden
Output

## Slide 17: Proposed models

## Slide 18: Encoder-Decoder LSTM
Notes: No images

## Slide 19: Sequential CNN
Notes: No PR

## Slide 20: CNN-LSTM [img]

## Slide 21: CNN-LSTM [img+PR]
Notes: Also, img only

## Slide 22: Encoder-Decoder LSTM
Notes: Encoder decoder LSTM, consistent accuracy

## Slide 23: LSTM CNN [img-PR]
Notes: IMG PR LSTM CNN

## Slide 24: Sequential CNN
Notes: Sequential CNN

## Slide 25: Optimized results
Model name | IO-ratio | Inference time | Avg. PR error | Trainable parameters
Encoder-Decoder LSTM* | 120/60 | 155ms | 2° | 1.211.010
Sequential CNN | 10/30 | 4.203ms | 5,79° | 98.639.180
CNN LSTM [img] | 10/120 | 4.042ms | 1,73° | 217.659.752
CNN LSTM [img] (gray) | 10/120 | 3.545ms | 1,71° | 217.659.352
CNN LSTM [img-PR] | 10/120 | 4.453ms | 1,72° | 217.741.672
CNN LSTM [img-PR] (gray) | 10/120 | 3.797ms | 1,81° | 217.741.272

## Slide 26: Optimized results
Model name | IO-ratio | Inference time | Avg. PR error | Trainable parameters
Encoder-Decoder LSTM* | 120/60 | 155ms | 2° | 1.211.010
Sequential CNN | 10/30 | 4.203ms | 5,79° | 98.639.180
CNN LSTM [img] | 10/120 | 4.042ms | 1,73° | 217.659.752
CNN LSTM [img] (gray) | 10/120 | 3.545ms | 1,71° | 217.659.352
CNN LSTM [img-PR] | 10/120 | 4.453ms | 1,72° | 217.741.672
CNN LSTM [img-PR] (gray) | 10/120 | 3.797ms | 1,81° | 217.741.272
Notes: Up to 120 second prediction, low 10% relative error, good inference time

## Slide 27: Optimized results
Model name | IO-ratio | Inference time | Avg. PR error | Trainable parameters
Encoder-Decoder LSTM* | 120/60 | 155ms | 2° | 1.211.010
Sequential CNN | 10/30 | 4.203ms | 5,79° | 98.639.180
CNN LSTM [img] | 10/120 | 4.042ms | 1,73° | 217.659.752
CNN LSTM [img] (gray) | 10/120 | 3.545ms | 1,71° | 217.659.352
CNN LSTM [img-PR] | 10/120 | 4.453ms | 1,72° | 217.741.672
CNN LSTM [img-PR] (gray) | 10/120 | 3.797ms | 1,81° | 217.741.272
Notes: Suffers from not having LSTM, high inference time, low IO still high error

## Slide 28: Optimized results
Model name | IO-ratio | Inference time | Avg. PR error | Trainable parameters
Encoder-Decoder LSTM* | 120/60 | 155ms | 2° | 1.211.010
Sequential CNN | 10/30 | 4.203ms | 5,79° | 98.639.180
CNN LSTM [img] | 10/120 | 4.042ms | 1,73° | 217.659.752
CNN LSTM [img] (gray) | 10/120 | 3.545ms | 1,71° | 217.659.352
CNN LSTM [img-PR] | 10/120 | 4.453ms | 1,72° | 217.741.672
CNN LSTM [img-PR] (gray) | 10/120 | 3.797ms | 1,81° | 217.741.272
Notes: Gray, little improvement in accuracy, high latency for all, much better with lstm

## Slide 29: Conclusion
Images contribute to …
  Marginal increase in accuracy
  Significant increase in latency
  Prone to occlusion/obstructions
LSTM module is crucial
Encoder-Decoder LSTM is the optimal model
  Up to 120 seconds
  2° error on average
  Consistent & equal accuracy

## Slide 30: Future work

## Slide 31: Real data
Video + IMU data (ZED-mini)
Additional inputs
  Angular velocity
  Wind speed/direction
  Thrust
Challenges:
  Optimal sample rate
  Objects in images
  Stabilization
  Noise

## Slide 32: Questions