## Slide 1: Ship motion prediction with IMU-data and images
Lance De Waele
Supervisors: Prof. dr. ir. Hiep Luong, Prof. dr. ir. Jan Aelterman
Counsellors: Charles Hamesse, Ir. Tien-Thanh Nguyen (Royal Military Academy), Dr. ir. Benoit Pairet (Royal Military Academy)

## Slide 2: Contents
Introduction
Goal & Incentive
Data
Deep learning
Proposed models
Results
Conclusion

## Slide 3: Introduction
Royal Military Academy
Robotics & Autonomous Systems lab
MarLand
  Developing an autonomous drone
  Vertical Take-off and landing (VTOL) on moving vessels
Notes: The Robotics & Autonomous Systems lab is a research unit of the department of Mechanics of the Belgian Royal Military Academy.

## Slide 4: Goal & Method
Safe VTOL procedures:
  Drone and surroundings
  Landing deck stabile and level
  Minimize impact
Predict the motion of the vessel
  Anticipate movements
Requirements:
  Optimized for application
  Minimum 30 seconds
  Low latency & HW requirements

## Slide 5: Ship Motion
Six degrees of freedom (DoF)
  Translational
    Sway
    Surge
    Heave

## Slide 6: Ship Motion
Six degrees of freedom (DoF)
  Translational
    Sway
    Surge
    Heave
  Rotational
    Yaw
    Pitch
    Roll

## Slide 7: Simulated data
540 episodes of 400 images
Rendered at 2 frames/second (2Hz)
  Overlap, processing demand
  Aliasing <-> Accuracy
  30 hours of simulation
Resolution 96x54
Pitch & Roll (PR) per image
No heave?
₁Source: https://github.com/Nazotron1923/ship-ocean_simulation_BLENDER
Notes: Why only pitch and roll is enough:
Drone has large range of motion in heave but very small window in vertical hover pitch and roll
Lightweight drone with low inertia/high thrust can heave up/down based on measurements in real time

## Slide 8: Properties
Property | Pitch | Roll
count | 216.000 | 216.000
mean | 0,07° | 0,30°
standard deviation | 6,6° | 7,1°
minimum | -53,7° | -58,8°
25% | -2,7° | -2,6°
50% | 0,03° | 0,23°
75% | 2,8° | 3,2°
maximum | 61,3° | 62,2°
Notes: First, count: 540 episodes, each with 400 frames equals to 216k total images
Second, mean and median are equal, near zero
Third, stdev from roll is slightly higher than pitch => more spread-out values
Minimum and maximum similar and

## Slide 9: Properties
Property | Pitch | Roll
count | 216.000 | 216.000
mean | 0,07° | 0,30°
standard deviation | 6,6° | 7,1°
minimum | -53,7° | -58,8°
25% | -2,7° | -2,6°
50% | 0,03° | 0,23°
75% | 2,8° | 3,2°
maximum | 61,3° | 62,2°
400 frames/episode * 540 episodes
Notes: First, count: 540 episodes, each with 400 frames equals to 216k total images
Second, mean and median are equal, near zero
Third, stdev from roll is slightly higher than pitch => more spread-out values
Minimum and maximum similar and

## Slide 10: Properties
Property | Pitch | Roll
count | 216.000 | 216.000
mean | 0,07° | 0,30°
standard deviation | 6,6° | 7,1°
minimum | -53,7° | -58,8°
25% | -2,7° | -2,6°
50% | 0,03° | 0,23°
75% | 2,8° | 3,2°
maximum | 61,3° | 62,2°
Notes: First, count: 540 episodes, each with 400 frames equals to 216k total images
Second, mean and median are equal, near zero. Ship naturally wants to remain upright, symmetrical distributions
Third, stdev from roll is slightly higher than pitch => more spread-out values
Minimum and maximum similar and

## Slide 11: Properties
Property | Pitch | Roll
count | 216.000 | 216.000
mean | 0,07° | 0,30°
standard deviation | 6,6° | 7,1°
minimum | -53,7° | -58,8°
25% | -2,7° | -2,6°
50% | 0,03° | 0,23°
75% | 2,8° | 3,2°
maximum | 61,3° | 62,2°
Notes: First, count: 540 episodes, each with 400 frames equals to 216k total images
Second, mean and median are equal, near zero
Third, stdev from roll is slightly higher than pitch => more spread-out values
Minimum and maximum similar and

## Slide 12: Properties
Property | Pitch | Roll
count | 216.000 | 216.000
mean | 0,07° | 0,30°
standard deviation | 6,6° | 7,1°
minimum | -53,7° | -58,8°
25% | -2,7° | -2,6°
50% | 0,03° | 0,23°
75% | 2,8° | 3,2°
maximum | 61,3° | 62,2°
Notes: First, count: 540 episodes, each with 400 frames equals to 216k total images
Second, mean and median are equal, near zero
Third, stdev from roll is slightly higher than pitch => more spread-out values
Minimum and maximum similar and around 60: good perspective of the conditions of the vessel

## Slide 13: Properties
99.7% : µ ± 3σ ≈ [-20°, 20°]
Notes: Both pitch and roll are normally distributed, 99.7% in interval [-20°, 20°]

## Slide 14: Pre-processing

## Slide 15: Deep learning

## Slide 16: Deep learning
Neural networks
Layers of neurons
Neurons learn
  Weight (w)
  Bias (b)
  Y = wx + b
x
Y

## Slide 17: Deep learning
IMU data
Predicted sequence
Input
Hidden
Output

## Slide 18: Neural network architectures
Continuous data -> linear regression
  <-> logistic regression
Time series data -> LSTM
  Feedback connections
Images -> CNN
  Moving image kernels

## Slide 19: Optimal architecture?
Inputs ?
Hidden layers ?
Hyperparameters ?
Input
Hidden
Output

## Slide 20: Proposed models

## Slide 21: Encoder-Decoder LSTM
Notes: No images

## Slide 22: Sequential CNN
Notes: No PR

## Slide 23: CNN-LSTM [img]

## Slide 24: CNN-LSTM [img+PR]
Notes: Also, img only

## Slide 25: Encoder-Decoder LSTM
Notes: Encoder decoder LSTM, consistent accuracy

## Slide 26: LSTM CNN [img-PR]
Notes: IMG PR LSTM CNN

## Slide 27: Sequential CNN
Notes: Sequential CNN

## Slide 28: Optimized results
Model name | IO-ratio | Inference time | Avg. PR error | Trainable parameters
Encoder-Decoder LSTM* | 120/60 | 155ms | 2° | 1.211.010
Sequential CNN | 10/30 | 4.203ms | 5,79° | 98.639.180
CNN LSTM [img] | 10/120 | 4.042ms | 1,73° | 217.659.752
CNN LSTM [img] (gray) | 10/120 | 3.545ms | 1,71° | 217.659.352
CNN LSTM [img-PR] | 10/120 | 4.453ms | 1,72° | 217.741.672
CNN LSTM [img-PR] (gray) | 10/120 | 3.797ms | 1,81° | 217.741.272

## Slide 29: Optimized results
Model name | IO-ratio | Inference time | Avg. PR error | Trainable parameters
Encoder-Decoder LSTM* | 120/60 | 155ms | 2° | 1.211.010
Sequential CNN | 10/30 | 4.203ms | 5,79° | 98.639.180
CNN LSTM [img] | 10/120 | 4.042ms | 1,73° | 217.659.752
CNN LSTM [img] (gray) | 10/120 | 3.545ms | 1,71° | 217.659.352
CNN LSTM [img-PR] | 10/120 | 4.453ms | 1,72° | 217.741.672
CNN LSTM [img-PR] (gray) | 10/120 | 3.797ms | 1,81° | 217.741.272
Notes: Up to 120 second prediction, low 10% relative error, good inference time

## Slide 30: Optimized results
Model name | IO-ratio | Inference time | Avg. PR error | Trainable parameters
Encoder-Decoder LSTM* | 120/60 | 155ms | 2° | 1.211.010
Sequential CNN | 10/30 | 4.203ms | 5,79° | 98.639.180
CNN LSTM [img] | 10/120 | 4.042ms | 1,73° | 217.659.752
CNN LSTM [img] (gray) | 10/120 | 3.545ms | 1,71° | 217.659.352
CNN LSTM [img-PR] | 10/120 | 4.453ms | 1,72° | 217.741.672
CNN LSTM [img-PR] (gray) | 10/120 | 3.797ms | 1,81° | 217.741.272
Notes: Suffers from not having LSTM, high inference time, low IO still high error

## Slide 31: Optimized results
Model name | IO-ratio | Inference time | Avg. PR error | Trainable parameters
Encoder-Decoder LSTM* | 120/60 | 155ms | 2° | 1.211.010
Sequential CNN | 10/30 | 4.203ms | 5,79° | 98.639.180
CNN LSTM [img] | 10/120 | 4.042ms | 1,73° | 217.659.752
CNN LSTM [img] (gray) | 10/120 | 3.545ms | 1,71° | 217.659.352
CNN LSTM [img-PR] | 10/120 | 4.453ms | 1,72° | 217.741.672
CNN LSTM [img-PR] (gray) | 10/120 | 3.797ms | 1,81° | 217.741.272
Notes: Gray, little improvement in accuracy, high latency for all, much better with lstm

## Slide 32: Conclusion
Images contribute to …
  Marginal increase in accuracy
  Significant increase in latency
  Prone to occlusion/obstructions
LSTM module is crucial
Encoder-Decoder LSTM is the optimal model
  Up to 120 seconds
  2° error on average
  Consistent & equal accuracy

## Slide 33: Future work

## Slide 34: Real data
Video + IMU data (ZED-mini)
Additional inputs
  Angular velocity
  Wind speed/direction
  Thrust
Challenges:
  Optimal sample rate
  Objects in images
  Stabilization
  Noise

## Slide 35: Questions