## Slide 1: Ship motion prediction with IMU-data and images
Lance De Waele
Supervisors:
Prof. dr. ir. Hiep Luong
Prof. dr. ir. Jan Aelterman
Counselors:
Charles Hamesse
Ir. Tien-Thanh Nguyen (Royal Military Academy)
Dr. ir. Benoit Pairet (Royal Military Academy)

## Slide 2: Contents
Introduction
Goal & Incentive
Data
Deep learning
Proposed models
Results
Conclusion

## Slide 3: Introduction
Royal Military Academy
Robotics & Autonomous Systems lab
MarLand
  Developing an autonomous helicopter-type drone
  Vertical Take-off and Landing (VTOL) on Belgian navy vessels
Notes: The Robotics & Autonomous Systems lab is a research unit of the department of Mechanics of the Belgian Royal Military Academy.

## Slide 4: Situation
Goal:
→ Safe and autonomous VTOL on Navy vessels
Problem:
→ Seaborne vessels are instable due to wave-induced motions
Proposed solution:
→ Predict motion of the vessel to anticipate movement
Notes: Safety:
both drone itself and its surroundings
Minimize impact => Landing deck must be stabile and level
Problem:
Ship is moving due wind and currents but mainly due to ocean waves, causing uncontrollable instability of the landing deck
Solution:
Predict motion so we can avoid collision by anticipating future movements, not only of the landing platform, but also of the surroundings (antennas)
Other solutions
Dampen wave motions with (outside scope)

## Slide 5: Situation
How ?
→ Deep neural networks
→ IMU data & wave images
Requirements:
  Optimized for application
  Minimum 30 seconds
  Low latency & HW demand
Notes: Train deep neural networks to map input of motions to a series of output motions
Predictions are facilitated by an onboard inertial measurement unit (IMU) and a front facing camera capturing incoming wave images
Optimized for drone VTOL and images and sensory data available
We want to be able to predict at least 30 seconds into the future to provide the drone with ample time to initiate a VTOL procedure: move in place, descend, ascend, move away
System needs to be lightweight to run on current hardware and not demand a lot of resources: both memory and compute, latency should be low to allow for quick corrections and continuous predictions

## Slide 6: Ship Motion
Six Degrees of Freedom (DoF)
  Translational
    Sway
    Surge
    Heave
Notes: The motion of any rigid object can be expressed in 6 degrees of freedom. These 6 DOF describe the 3D orientation of the object
They can be divided in two categories: translational and rotational.
Translational are expressed in distance units
Sway: lateral left and right movement - currents, wind, sidethruster
Surge: front and backwards movement - thrust of the vessel
Heave: up and downwards motion - wave induced motion

## Slide 7: Ship Motion
Six Degrees of Freedom (DoF)
  Translational
    Sway
    Surge
    Heave
  Rotational
    Yaw
    Pitch
    Roll
Notes: Rotational degrees of freedom are expressed in angular units
Yaw: steering of the vessel
Pitch: wave induced
Roll: wave induced

## Slide 8: Ship Motion
Six Degrees of Freedom (DoF)
  Translational
    Sway
    Surge
    Heave
  Rotational
    Yaw
    Pitch
    Roll
Notes: These 6 DoF describe the 3D orientation of the vessel and when measured over a sequence of time they describe the motion of the vessel. This motion can than be extended into the future by predictions
Three targets are selected:
Heave: impact
Pitch and roll: stability

## Slide 9: Sensor setup
ZED-mini:
Inertial Measurement Unit (IMU)
  Translational
  Rotational
  Angular velocities
Stereo Camera
  Incoming waves

## Slide 10: Simulated data
540 episodes of 400 frames each
Rendered at 2 frames/second (2Hz)
  Overlap, processing demand
  Aliasing ⥈ Accuracy
  30 hours of simulation
Resolution 96x54
Pitch & Roll (PR) per image
No heave
₁Source: https://github.com/Nazotron1923/ship-ocean_simulation_BLENDER
Notes: BLENDER SIMULATION
Justification for no heave:
Drone has large range of motion in heave but very small window in vertical hover pitch and roll
Lightweight drone with low inertia/high thrust can heave up/down based on measurements in real time

## Slide 11: Simulated data
Notes: Eén keer klikken once op deze slide

## Slide 12: Simulation parameters
Daytime, clear weather
Sensor orientation
  Height: 5m
  Rotation: 76°
Varying ocean conditions
  Sea depth
  Wind velocity
  Wave alignment
  Choppiness
Notes: Slightly tilted or pitch downwards
Sea depth influence the wave height

## Slide 13: Properties
99.7% : µ ± 3σ ≈ [-21°, 21°]
216.000 frames
  540ep*400f
Symmetric around 0°
No skew
→ Normally distributed
Notes: Both pitch and roll are normally distributed, 99.7% in interval [-20°, 20°]

## Slide 14: Pre-processing: sequencing
Notes: s = 400 for simulated dataset en oneindig voor real-time data
Eerste 5 frames als input, een forward prediction voorspelt 5 nieuwe frames

## Slide 15: Pre-processing: sequencing
Optimal input-output (IO) ratio?
Notes: Optimal IO-ratio?

## Slide 16: Deep neural networks
Modern and accessible
Facilitate …
  Image processing
  Continuous output
  Time series data
→ Need for comprehensive ensemble of architectures

## Slide 17: Neural network architectures: LSTM
Long-Short Term Memory network
Recurrent NN
Maintains two memory states
LSTM cell: 4 gates
Coupled sequentially

## Slide 18: Neural network architectures: CNN
Convolutional Neural Network
Efficient for image processing
Convolving weighted kernels across image
Learns kernel weights for optimal feature extraction

## Slide 19: Optimal architecture ?
Inputs: images and/or IMU ?
Architectures: CNN, LSTM ?
Hyperparameters: IO-ratio, hidden size ?

## Slide 20: Proposed models

## Slide 21: Encoder-Decoder LSTM
Layer | Input dim.
LSTM | 2 x N
LSTM | 2 x 300
Linear | 2 x 300
Linear | 2 x 150
Output | 2 x M
Notes: No images

## Slide 22: Sequential CNN
Layer | Input dim.
Conv2D | 3 x 54 x 96
ReLu | 8 x 54 x 96
MaxPooling | 8 x 54 x 96
Conv2D | 8 x 27 x 48
ReLu | 16 x 27 x 48
MaxPooling | 16 x 27 x 48
Conv2D | 16 x 13 x 24
ReLu | 32 x 13 x 24
MaxPooling | 32 x 13 x 24
Linear | 1 x N*2304
Linear | 1 x 4096
Linear | 1 x 1024
Tanh | 1 x 2*M
Output | 2 x M
Notes: No PR

## Slide 23: CNN-LSTM [img]
Layer | Input dim.
Conv2D | 3 x 54 x 96
ReLu | 8 x 54 x 96
MaxPooling | 8 x 54 x 96
Conv2D | 8 x 27 x 48
ReLu | 16 x 27 x 48
MaxPooling | 16 x 27 x 48
LSTM | 1 x N*4992
LSTM | 1 x 1024
Linear | 1 x 1024
Linear | 1 x 512
Tanh | 1 x 2*M
Output | 2 x M

## Slide 24: CNN LSTM [img+PR]
Layer | Input dim.
Conv2D | 3 x 54 x 96
ReLu | 8 x 54 x 96
MaxPooling | 8 x 54 x 96
Conv2D | 8 x 27 x 48
ReLu | 16 x 27 x 48
MaxPooling | 16 x 27 x 48
LSTM | 1 x N*4994
LSTM | 1 x 1024
Linear | 1 x 1024
Linear | 1 x 512
Tanh | 1 x 2*M
Output | 2 x M
Notes: Also, img only

## Slide 25: Prediction results
IO-ratios: 60/60 & 10/60
  Real pitch (blue)
  Predicted pitch (red)
Encoder-decoder LSTM – 60/60
Sequential CNN – 10/60
LSTM CNN [img+PR] – 10/60
Notes: CONSISTENT Accuracy

## Slide 26: IO-ratio optimization
 | IO-ratio | Avg. Pitch error [denormalized RMSE] | Avg. Roll error [denormalized RMSE]
 | 10/60 | 4,43° | 4,02°
 | 20/60 | 3,34° | 2,98°
 | 30/60 | 2,92° | 2,59°
 | 40/60 | 2,68° | 2,38°
 | 50/60 | 2,58° | 2,3°
 | 60/60 | 2,46° | 2,2°
 | 90/60 | 2,2° | 2,09°
 | 120/60 | 2,02° | 1,98°
 | zero-prediction | 6,43° | 7,30°

## Slide 27: Optimized results
Model name | IO-ratio | Inference time | Avg. PR error | Trainable parameters
Encoder-Decoder LSTM | 120/60 | 155ms | 2° | 1 211 010
Sequential CNN | 10/30 | 4 203ms | 5.79° | 98 639 180
CNN LSTM [img] | 10/120 | 4 042ms | 1.73° | 217 659 752
CNN LSTM [img] (gray) | 10/120 | 3 545ms | 1.71° | 217 659 352
CNN LSTM [img-PR] | 10/120 | 4 453ms | 1.72° | 217 741 672
CNN LSTM [img-PR] (gray) | 10/120 | 3 797ms | 1.81° | 217 741 272

## Slide 28: Optimized results
Model name | IO-ratio | Inference time | Avg. PR error | Trainable parameters
Encoder-Decoder LSTM | 120/60 | 155ms | 2° | 1 211 010
Sequential CNN | 10/30 | 4 203ms | 5.79° | 98 639 180
CNN LSTM [img] | 10/120 | 4 042ms | 1.73° | 217 659 752
CNN LSTM [img] (gray) | 10/120 | 3 545ms | 1.71° | 217 659 352
CNN LSTM [img-PR] | 10/120 | 4 453ms | 1.72° | 217 741 672
CNN LSTM [img-PR] (gray) | 10/120 | 3 797ms | 1.81° | 217 741 272
Notes: Up to 120 second prediction, low 10% relative error, good inference time

## Slide 29: Optimized results
Model name | IO-ratio | Inference time | Avg. PR error | Trainable parameters
Encoder-Decoder LSTM | 120/60 | 155ms | 2° | 1 211 010
Sequential CNN | 10/30 | 4 203ms | 5.79° | 98 639 180
CNN LSTM [img] | 10/120 | 4 042ms | 1.73° | 217 659 752
CNN LSTM [img] (gray) | 10/120 | 3 545ms | 1.71° | 217 659 352
CNN LSTM [img-PR] | 10/120 | 4 453ms | 1.72° | 217 741 672
CNN LSTM [img-PR] (gray) | 10/120 | 3 797ms | 1.81° | 217 741 272
Notes: Suffers from not having LSTM, high inference time, low IO still high error

## Slide 30: Optimized results
Model name | IO-ratio | Inference time | Avg. PR error | Trainable parameters
Encoder-Decoder LSTM | 120/60 | 155ms | 2° | 1 211 010
Sequential CNN | 10/30 | 4 203ms | 5.79° | 98 639 180
CNN LSTM [img] | 10/120 | 4 042ms | 1.73° | 217 659 752
CNN LSTM [img] (gray) | 10/120 | 3 545ms | 1.71° | 217 659 352
CNN LSTM [img-PR] | 10/120 | 4 453ms | 1.72° | 217 741 672
CNN LSTM [img-PR] (gray) | 10/120 | 3 797ms | 1.81° | 217 741 272
Notes: Gray, little improvement in accuracy, high latency for all, much better with lstm

## Slide 31: Augmented data tests
400 frames of augmented data: manual ink blots
Simulate obstruction/occlusion
Worst case scenario
CNN LSTM trained on normal data
→ Tested on augmented data

## Slide 32
CNN LSTM [img] prediction on augmented frames: grayscale (left) and colored (right)
CNN LSTM [img+PR] prediction on augmented frames: grayscale (left) and colored (right)
Notes: Pitch only

## Slide 33: Conclusion
Images contribute to …
  Marginal increase in accuracy
  Significant increase in latency & memory
  Prone to occlusion/obstructions
LSTM module is crucial
Encoder-Decoder LSTM is the optimal model
  Up to 120 seconds
  2° error on average
  Consistent & equal accuracy

## Slide 34: Future work

## Slide 35: Real data
Live video + IMU data (ZED-mini)
Additional inputs
  Angular velocity
  Wind speed/direction
  Thrust
Challenges:
  Optimal sample rate
  Objects in images
  Stabilization
  Noise

## Slide 36: Questions